Colour Printer Power

www.jensin.cn

JA346OKA

·241 W Fan Cooled

·383W Peak Rating for 500 ms

·Efficiency up to 80%

·AC OUT 600W Peak

·5 V Standby Rail and Inhibit Function

·Size: 192(L) X190(W) X 60(H)mm

·UL\CSA Safety Approvals

·10 Year Warranty

GREEN·POWER

Specification

| Input |
| --- |
| input Voltage | ·85-138 VAC/187-276 VAC |
| Input Frequency | ·47-63 Hz |
| Input Current | ·3.7 A max at 100 VAC, full load ·1.6 A max at 230 VAC, full load |
| Inrush Current | ·45 A max at 230 VAC, ·20 A max at 100 VAC, cold start at 25 °C |
| Input Protection | ·100VAC：Internal T20A250V、T8A250V and 1A250V fuse inLine and neutral ·230VAC：Internal T10A250V and T4A250V fuse inLine and neutral |
| Output |
| Output Voltage | ·V1:5.1 VDC,V2:24VDC,V3:5VSDC |
| Output Current | ·9A V1,8A V2,1A V3 |
| Output Voltage Trim | ·±3%V1,±3%V2,±3%V3 |
| Initial Set Accuracy | ·±0.5% V1 |
| Minimum Load | ·0.03A V1; 0A V2; 0.03A V3 |
| Max Load | ·13A V1; 13A V2; 1.2A V3 |
| Start Up Delay | ·1.6S max |
| Start Up Rise Time | ·0.1S max |
| Hold Up Time | ·20 ms min at 100 VAC or 220VAC |
| Temperature Drift | ·±0.2% after 20 min warm up |
| Line Regulation | ·±0.5% max |
| Load Regulation | ·±1% V1, ±1% V2, ±1% V3 |
| TransientResponse | ·2% max. deviation, recovery to within 1% in 500 µs for a 50-75-50% load change |
| Ripple & Noise | ·300mV pk-pk, bandwidth full |
| Overvoltage Protection | ·7V max V1, 31V max V2; 7V max V3; (V1、V2、V3 Latch Off ) |
| Overload Protection | ·15A max V1,18A max V2,3A max V3 (V1、V2、V3 Latch Off) |
| Short Circuit Protection | ·Latch Off（V1、V2、V3） |
| Temperature protection | ·100℃ max Latch Off |
| General |
| Efficiency | ·Up to 80% at rating load |
| Isolation | ·3300 VAC 2S Input to Output, 3300 VAC 2S Input to Ground, |
| Control Signals | ·HEATON-N and ACZEROCROSS |
| MTBF | ·100000H or more |
| Environmental |
| Operating Temperature | ·0 °C to +50 °C |
| Cooling | ·Fan cooled |
| Operating Humidity | ·15-90% RH, non-condensing |
| Storage Temperature | ·-10 °C to +65 °C Non binding |
| Operating Altitude | ·3000 m max |
| Shock | ·Operating 5g, No Operating 30g, X, Y, Z in each direction, each of the 3 back |
| Vibration | ·Operating 0.5g, 5-100Hz,20 minutes ·No Operating 2g, 10-550Hz,30 minutes |
| EMC & Safety |
| Emissions | ·EN55022 Class B、VCC I Class B 、FCC Class B EN55024 Class B、IEC6100-3、EN6100-3 |
| Surge | ·IEC1000-4-5 |
| Safety Approvals(100-127V) | ·J60950(H19),UL60950-1, JISC6950:2006, CAN/CSA,C22.2No.60950-1-07 |
| Safety Approvals(220-240V) | ·LVD 2006/95/EC,EN60950-1:2006 |

# Text boxes

SHENZHEN CEC PANDA JENSIN TECHNOLOGY CO., LTD

AC DC